## Slide 1: Joystick-Controlled 2-DOF Robotic Arm
Arduino-Based Project Presentation
January 2026

## Slide 2: What is a Robotic Arm?

## Slide 3: Definition & Basics
A robotic arm is a programmable mechanical arm that mimics the functions of a human arm.
Used in industry for precision tasks (welding, assembly, picking).
In education/hobby projects: Built with servo motors for controlled movement.
Degrees of Freedom (DOF): Number of independent movements.
  This project: 2 DOF (Base rotation + Arm lift)

## Slide 4: Project Inspiration

## Slide 5: Real-World Examples
Joystick-controlled robotic arms in action

## Slide 6: Similar Projects
MeArm-style joystick control

## Slide 7: Simple 2-DOF Designs
Basic servo-based arm

## Slide 8
Professional 2-DOF build guide

## Slide 9: Components Used

## Slide 10: Key Hardware
Arduino Uno/Nano
2 × Hobby Servo Motors (e.g., SG90/MG90S)
  Base servo (low load)
  Arm servo (higher load - 'hanged')
Analog Joystick Module (XY axes)
Breadboard & Jumper Wires
External Power: 2× 3.7V batteries (~7.4V) or 4× AA
Optional: Capacitor for power stability

## Slide 11: Joystick Module
Dual-axis analog joystick

## Slide 12: Wiring & Power

## Slide 13: Connections
Joystick: GND → GND, +5V → 5V, VRx → A0, VRy → A1
Servos: Signal → Pins 3 & 5
  Power (red) → External battery +
  Ground → External battery - + Arduino GND (common ground!)
Critical: External power prevents lag under load

## Slide 14: Wiring Diagram
Joystick & Arduino connections

## Slide 15: External Power Setup
Safe servo powering with common ground

## Slide 16: Arduino Code

## Slide 17: Complete Code
#include <Servo.h> Servo servoBase; // Base Servo servoArm; // Arm int joyX = A0; int joyY = A1; int currentPosBase = 90; int currentPosArm = 90; void setup() { servoBase.attach(3); servoArm.attach(5); servoBase.write(90); servoArm.write(90); } void loop() { int targetBase = map(analogRead(joyX), 0, 1023, 0, 180); int targetArm = map(analogRead(joyY), 0, 1023, 0, 180); // Smooth incremental movement if (currentPosBase < targetBase) currentPosBase++; else if (currentPosBase > targetBase) currentPosBase--; if (currentPosArm < targetArm) currentPosArm++; else if (currentPosArm > targetArm) currentPosArm--; servoBase.write(currentPosBase); servoArm.write(currentPosArm); delay(15); }

## Slide 18: How It Works & Troubleshooting

## Slide 19: Operation
Joystick → Analog values (0-1023)
Mapped to 0-180° servo angles
Incremental steps (±1°) for smooth motion
External power solves lag on loaded servo

## Slide 20: Lessons Learned
Issue: Arm servo laggy → USB power insufficient
Fix: External batteries + common ground
Tip: Always separate power for loaded servos

## Slide 21: Thank You!
Project Complete & Fully Functional
Ready for expansions (gripper, more DOF)
Questions?